## Slide 1
Showcase of the offered fundamental curve shapes

## Slide 2
help PESCurve;
Showcase of the offered PES model curves
Use the PESCurve() function to generate a generalised PES model curve, defining a primary and spin-orbit split component.
A linear combination of these can be used to fit XPS data.
See ‘Example_003_PES_Model_Curves.mlx’ Live Script for examples.
PES Curve convolved with FDD at Fermi-edge
PES Curve generated from the layer summation of a potential profile, enveloped over the IMFP.

## Slide 3
Showcase of the offered PES background curves
Use the PESBackground() function to call any of these background subtraction methods; polynomial, Shirley and linear step functions.
See ‘Example_003_PES_Background_Curves.mlx’ Live Script for example on how to use.
help PESBackground;

## Slide 4
Simulating the photoelectron intensity contributions of an N-layered sample
Tools can be used to fit the photon energy dependence of PES data.
nlayer_pes_model() function to simulate photoelectron intensity contributions of an N-layer model.
view_nlayer_pes_model() to quickly view solved model.
view_nlayer_sample() to quickly view the defined N-layer model sample stack.
overlayer_calc() to determine thickness of an overlayer on a bulk substrate using PES.
pes_model_2L = nlayer_pes_model(500:1200, {'SiO2', 'Si'}, {'Si(2p)', 'Si(2p)'}, {2.0, Inf});
See ‘Example_020_Multilayer_PES_Modelling.mlx’ Live Script for example on how to use.

## Slide 5
Showcase of curve fitting photoelectron spectroscopy data
Peak location finder
Peak FWHM finder
Fitting FDD for EB reference
= 550 eV
= 1150 eV
Example
Example
See ‘Example_021-022_PES_Data_Fitting.mlx’ Live Script for an example on how to run the PES fitting routines.

## Slide 6
(1) Eb alignment
(2) Background subtraction
(3) AngleWavevectors
Showcase of the offered ARPES data processing tools
See ‘Example_010-012_ARPES_EbKx_Processing.mlx’ Live Script on a step-by-step guide to process ARPES data.
Final ARPES data after processing
MDC Cut Series
Kf extraction using maximum gradient method

## Slide 7
(2) Eb alignment
(3) AngleWavevectors
(1) 3D ARPES data
IsoE Slicing
IsoK Slicing
Showcase of curve fitting ARPES data
See ‘Example_010-012_ARPES_KxKz_Branched_Processing.mlx’ Live Script for another example.
MDC Cut Series of IsoE Slice
Extracting electron pocket properties
IsoE Slice with BZ overlay

## Slide 8
Showcase of the offered ARPES model curves
3 subbands example
See ‘Example_003_ARPES_Model_Curves.mlx’ Live Script for example on how to use.

## Slide 9
Showcase of curve fitting ARPES data
See ‘Example_013_ARPES_EbKx_Fitting.mlx’ Live Script for an example on how to run the ARPES fitting routines.
Fit VB to Leading Edge
Fit VB to Leading Peak
-0.564 eV
-0.773 eV
Fit CB to N-Parabolas
MODEL
DATA

## Slide 10
HX-ARPES regime
2000 – 6000 eV
SX-ARPES regime 310 – 1600 eV
UV-ARPES regime 10 – 200 eV
Brillouin Zone Navigation: Relating photon energy to
See ‘Example_002_BZ_Navigation.mlx’ Live Script for an example.
extract_lattice()
extract_bz_overlay()
extract_hv_overlay()